## Slide 1: Chapter 6
Parallel Processors from Client to Cloud

## Slide 2: Introduction
Goal: connecting multiple computers to get higher performance
  Multiprocessors
  Scalability, availability, power efficiency
Job-level (process-level) parallelism
  High throughput for independent jobs
Parallel processing program
  Single program run on multiple processors
Multicore microprocessors
  Chips with multiple processors (cores)
§6.1 Introduction

## Slide 3: Hardware and Software
Hardware
  Serial: e.g., Pentium 4
  Parallel: e.g., Intel Core i7
Software
  Sequential: e.g., matrix multiplication
  Concurrent: e.g., operating system
Sequential/concurrent software can run on serial/parallel hardware
  Challenge: making effective use of parallel hardware

## Slide 4: What We’ve Already Covered
§2.11: Parallelism and Instructions
  Synchronization
§3.6: Parallelism and Computer Arithmetic
  Subword Parallelism
§4.10: Parallelism via Instructions
§5.10: Parallelism and Memory Hierarchies
  Cache Coherence

## Slide 5: Parallel Programming
Parallel software is the problem
Need to get significant performance improvement
  Otherwise, just use a faster uniprocessor, since it’s easier!
Difficulties
  Partitioning
  Coordination
  Communications overhead
§6.2 The Difficulty of Creating Parallel Processing Programs

## Slide 6: Amdahl’s Law
Sequential part can limit speedup
Example: 100 processors, 90× speedup?
  Tnew = Tparallelizable/100 + Tsequential
  Solving: Fparallelizable = 0.999
Need sequential part to be 0.1% of original time

## Slide 7: Scaling Example
Workload: sum of 10 scalars, and 10 × 10 matrix sum
  Speed up from 10 to 100 processors
Single processor: Time = (10 + 100) × tadd
10 processors
  Time = 10 × tadd + 100/10 × tadd = 20 × tadd
  Speedup = 110/20 = 5.5 (55% of potential)
100 processors
  Time = 10 × tadd + 100/100 × tadd = 11 × tadd
  Speedup = 110/11 = 10 (10% of potential)
Assumes load can be balanced across processors

## Slide 8: Scaling Example (cont)
What if matrix size is 100 × 100?
Single processor: Time = (10 + 10000) × tadd
10 processors
  Time = 10 × tadd + 10000/10 × tadd = 1010 × tadd
  Speedup = 10010/1010 = 9.9 (99% of potential)
100 processors
  Time = 10 × tadd + 10000/100 × tadd = 110 × tadd
  Speedup = 10010/110 = 91 (91% of potential)
Assuming load balanced

## Slide 9: Strong vs Weak Scaling
Strong scaling: problem size fixed
  As in example
Weak scaling: problem size proportional to number of processors
  10 processors, 10 × 10 matrix
    Time = 20 × tadd
  100 processors, 32 × 32 matrix
    Time = 10 × tadd + 1000/100 × tadd = 20 × tadd
  Constant performance in this example

## Slide 10: Instruction and Data Streams
An alternate classification
§6.3 SISD, MIMD, SIMD, SPMD, and Vector
 |  | Data Streams | 
 |  | Single | Multiple
Instruction Streams | Single | SISD: Intel Pentium 4 | SIMD: SSE instructions of x86
 | Multiple | MISD: No examples today | MIMD: Intel Xeon e5345
SPMD: Single Program Multiple Data
A parallel program on a MIMD computer
  Conditional code for different processors

## Slide 11: SIMD
Operate elementwise on vectors of data
  E.g., MMX and SSE instructions in x86
    Multiple data elements in 128-bit wide registers
All processors execute the same instruction at the same time
  Each with different data address, etc.
Simplifies synchronization
Reduced instruction control hardware
Works best for highly data-parallel applications

## Slide 12: Vector Processors
Highly pipelined function units
Stream data from/to vector registers to units
  Data collected from memory into registers
  Results stored from registers to memory
Example: Vector extension to RISC-V
  32 × 64-element registers (64-bit elements)
  Vector instructions
    fld.v, fsd.v: load/store vector
    fadd.d.v: add vectors of double
    fadd.d.vs: add scalar to each element of vector of double
Significantly reduces instruction-fetch bandwidth

## Slide 13: Example: DAXPY (Y = a × X + Y)
Conventional RISC-V code
fld f0,a(x3) // load scalar a addi x5,x19,512 // upper bound of what to load loop: fld f1,0(x19) // load x(i) fmul.d f1,f1,f0 // a × x(i) fld f2,0(x20) // load y(i) fadd.d f2,f2,f1 // a × x(i) + y(i) fsd f2,0(x20) // store into y(i) addi x19,x19,8 // increment index to x addi x20,x20,8 // increment index to y bltu x19,x5,loop // repeat if not done
Vector RISC-V code
fld f0,a(x3) // load scalar a fld.v v0,0(x19) // load vector x fmul.d.vs v0,v0,f0 // vector-scalar multiply fld.v v1,0(x20) // load vector y fadd.d.v v1,v1,v0 // vector-vector add fsd.v v1,0(x20) // store vector y

## Slide 14: Vector vs. Scalar
Vector architectures and compilers
  Simplify data-parallel programming
  Explicit statement of absence of loop-carried dependences
    Reduced checking in hardware
  Regular access patterns benefit from interleaved and burst memory
  Avoid control hazards by avoiding loops
More general than ad-hoc media extensions (such as MMX, SSE)
  Better match with compiler technology

## Slide 15: Multithreading
Performing multiple threads of execution in parallel
  Replicate registers, PC, etc.
  Fast switching between threads
Fine-grain multithreading
  Switch threads after each cycle
  Interleave instruction execution
  If one thread stalls, others are executed
Coarse-grain multithreading
  Only switch on long stall (e.g., L2-cache miss)
  Simplifies hardware, but doesn’t hide short stalls (eg, data hazards)
§6.4 Hardware Multithreading

## Slide 16: Simultaneous Multithreading
In multiple-issue dynamically scheduled processor
  Schedule instructions from multiple threads
  Instructions from independent threads execute when function units are available
  Within threads, dependencies handled by scheduling and register renaming
Example: Intel Pentium-4 HT
  Two threads: duplicated registers, shared function units and caches

## Slide 17: Multithreading Example

## Slide 18: Future of Multithreading
Will it survive? In what form?
Power considerations  simplified microarchitectures
  Simpler forms of multithreading
Tolerating cache-miss latency
  Thread switch may be most effective
Multiple simple cores might share resources more effectively

## Slide 19: Shared Memory
SMP: shared memory multiprocessor
  Hardware provides single physical address space for all processors
  Synchronize shared variables using locks
  Memory access time
    UMA (uniform) vs. NUMA (nonuniform)
§6.5 Multicore and Other Shared Memory Multiprocessors

## Slide 20: Example: Sum Reduction
Sum 100,000 numbers on 100 processor UMA
  Each processor has ID: 0 ≤ Pn ≤ 99
  Partition 1000 numbers per processor
  Initial summation on each processor
  sum[Pn] = 0; for (i = 1000*Pn; i < 1000*(Pn+1); i = i + 1) sum[Pn] = sum[Pn] + A[i];
Now need to add these partial sums
  Reduction: divide and conquer
  Half the processors add pairs, then quarter, …
  Need to synchronize between reduction steps

## Slide 21: Example: Sum Reduction
half = 100;
repeat
synch();
if (half%2 != 0 && Pn == 0)
sum[0] = sum[0] + sum[half-1];
/* Conditional sum needed when half is odd;
Processor0 gets missing element */
half = half/2; /* dividing line on who sums */
if (Pn < half) sum[Pn] = sum[Pn] + sum[Pn+half];
until (half == 1);

## Slide 22: History of GPUs
Early video cards
  Frame buffer memory with address generation for video output
3D graphics processing
  Originally high-end computers (e.g., SGI)
  Moore’s Law  lower cost, higher density
  3D graphics cards for PCs and game consoles
Graphics Processing Units
  Processors oriented to 3D graphics tasks
  Vertex/pixel processing, shading, texture mapping, rasterization
§6.6 Introduction to Graphics Processing Units

## Slide 23: Graphics in the System

## Slide 24: GPU Architectures
Processing is highly data-parallel
  GPUs are highly multithreaded
  Use thread switching to hide memory latency
    Less reliance on multi-level caches
  Graphics memory is wide and high-bandwidth
Trend toward general purpose GPUs
  Heterogeneous CPU/GPU systems
  CPU for sequential code, GPU for parallel code
Programming languages/APIs
  DirectX, OpenGL
  C for Graphics (Cg), High Level Shader Language (HLSL)
  Compute Unified Device Architecture (CUDA)

## Slide 25: Example: NVIDIA Tesla
Streaming multiprocessor
8 × Streaming processors

## Slide 26: Example: NVIDIA Tesla
Streaming Processors
  Single-precision FP and integer units
  Each SP is fine-grained multithreaded
Warp: group of 32 threads
  Executed in parallel, SIMD style
    8 SPs × 4 clock cycles
  Hardware contexts for 24 warps
    Registers, PCs, …

## Slide 27: Classifying GPUs
Don’t fit nicely into SIMD/MIMD model
  Conditional execution in a thread allows an illusion of MIMD
    But with performance degredation
    Need to write general purpose code with care
 | Static: Discovered at Compile Time | Dynamic: Discovered at Runtime
Instruction-Level Parallelism | VLIW | Superscalar
Data-Level Parallelism | SIMD or Vector | Tesla Multiprocessor

## Slide 28: Message Passing
Each processor has private physical address space
Hardware sends/receives messages between processors
§6.7 Clusters and Other Message-Passing Multiprocessors

## Slide 29: Loosely Coupled Clusters
Network of independent computers
  Each has private memory and OS
  Connected using I/O system
    E.g., Ethernet/switch, Internet
Suitable for applications with independent tasks
  Web servers, databases, simulations, …
High availability, scalable, affordable
Problems
  Administration cost (prefer virtual machines)
  Low interconnect bandwidth
    c.f. processor/memory bandwidth on an SMP

## Slide 30: Sum Reduction (Again)
Sum 100,000 on 100 processors
First distribute 100 numbers to each
  The do partial sums
  sum = 0; for (i = 0; i<1000; i = i + 1) sum = sum + AN[i];
Reduction
  Half the processors send, other half receive and add
  The quarter send, quarter receive and add, …

## Slide 31: Sum Reduction (Again)
Given send() and receive() operations
  limit = 100; half = 100;/* 100 processors */ repeat half = (half+1)/2; /* send vs. receive dividing line */ if (Pn >= half && Pn < limit) send(Pn - half, sum); if (Pn < (limit/2)) sum = sum + receive(); limit = half; /* upper limit of senders */ until (half == 1); /* exit with final sum */
  Send/receive also provide synchronization
  Assumes send/receive take similar time to addition

## Slide 32: Grid Computing
Separate computers interconnected by long-haul networks
  E.g., Internet connections
  Work units farmed out, results sent back
Can make use of idle time on PCs
  E.g., SETI@home, World Community Grid

## Slide 33: Interconnection Networks
Network topologies
  Arrangements of processors, switches, and links
§6.8 Introduction to Multiprocessor Network Topologies
Bus
Ring
2D Mesh
N-cube (N = 3)
Fully connected

## Slide 34: Multistage Networks

## Slide 35: Network Characteristics
Performance
  Latency per message (unloaded network)
  Throughput
    Link bandwidth
    Total network bandwidth
    Bisection bandwidth
  Congestion delays (depending on traffic)
Cost
Power
Routability in silicon

## Slide 36: Concluding Remarks
Goal: higher performance by using multiple processors
Difficulties
  Developing parallel software
  Devising appropriate architectures
Many reasons for optimism
  Changing software and application environment
  Chip-level multiprocessors with lower latency, higher bandwidth interconnect
An ongoing challenge for computer architects!
§6.14 Concluding Remarks