## Slide 1
Auxiliary Potential Functions and Reciprocity Theorem
Xing-Chang WEI
Zhejiang Univ., China
2011.12.05

## Slide 2
Introduction
The Vector Potential A for an Electric Current Source J
The Vector Potential F for an Magnetic Current Source M
Solution of the Inhomogeneous Vector Potential Wave Equation
Far-Field Radiation from Electric and Magnetic Currents
Duality Theorem
Reciprocity Theorem
Agenda

## Slide 3
Two methods to solve the electric and magnetic fields

## Slide 4
The most common vector potential functions are the A (magnetic vector potential) and F (electric vector potential). Another pair is the Hertz potentials Пe and Пh. In this lesson, we only talk about A and F.
Related to A and F are φ (electric scalar potential) and φm (magnetic scalar potential) respectively.
All potentials are strictly mathematical tools, they do not present any physically measurable variables.
The most difficult operation in the two-step procedure is the integration to determine A and F. Once A and F are known, then E and H can be easily determined by differentiation.

## Slide 5
Derive Magnetic Vector Potential A and Electrical Scalar Potential φ
The magnetic flux is always solenoidal (无散场)
because for any vector A we have
Substituting (3-2) into Maxwell’s curl equation
(3-3)
reduces it to
(3-5)
so that B can be represented as the curl of another vector A
or
(3-2)
(3-2a)
so that it can be represented as the gradient of another scalar φ
(3-7)
(3-7a)
or

## Slide 6
Substituting (3-13) into Maxwell’s equation leads to
(3-14)
The curl of A was defined, now we are at liberty to define the divergence of A, which is independent of its curl. We can define the following Lorentz condition
or
(3-13)
In addition
(3-15)
A: magnetic vector potential; φ: electric scalar potential
*
*

## Slide 7
Derive Electric Vector Potential F and Magnetic Scalar Potential φm
Magnetic current and charge do not exist in the nature. However, during the analysis of EM problem, we can
  Define some special electric current distribution as magnetic current;
  Define E field distribution as magnetic current when we use the volume or surface equivalence theorems.
Electric current J
Magnetic current M

## Slide 8
Define Electric Vector F
Define Magnetic Potential φm
Lorentz condition
Finally, the potential equation
H field is rewritten as

## Slide 9
Solution of the Inhomogeneous Vector Potential Wave Equation
Assume an infinitesimal source with current density Jz, only an Az component will exist.
(3-31)
At source-free(无源) region, where Jz=0, (3-31) reduces to
(3-32)
Jz

## Slide 10
Since in the limit the source is a point, it requires that Az is not a function of direction (θ and φ); in a spherical coordinate system, Az = Az(r) where r is the radial distance
(3-34)
* in the spherical coordinates system can be found in Appendix VII, page1085

## Slide 11
The differential equation of (3-34) has two independent solutions
(3-35)
wave traveling along r direction
wave traveling along -r direction
In the static case (ω = 0, k = 0), (3-35) simplifies to
(3-36)
We choose (3-35)
(3-38)
Thus in source-free region, the time-varying solution and the static solution of (3-35) and (3-38) differ only by the e−jkr factor
the time-varying solution of (3-35) can be obtained by multiplying the static solution of (3-38) by e−jkr

## Slide 12
In the presence of the source (Jz ≠0) and k = 0, the wave equation of (3-31) reduces to
(3-39)
Poisson’s Equation
The solution of Poisson’s equation is widely documented.
The most familiar equation with Poisson’s form is that relating the scalar electric potential φ to the electric charge density ρ.
which solution is

## Slide 13
(3-39)
of which the solution is
(3-42)
the time-varying solution can be obtained by multiplying the static solution of (3-42) by e−jkr
(3-43)

## Slide 14
(source) (3-44)
(3-46)
(source) (3-45)
(3-47)
(source) (3-31)
(3-43)

## Slide 15
Source Not At Origin
Source At Origin
(3-49)
(3-48)

## Slide 16
Volumetric Distributed
Current Densities
*

## Slide 17
When J has units of A/m2
M has units of V/m2
Then
(3-27)
(3-28)

## Slide 18
Surface Distributed
Current Densities
*

## Slide 19
When J has units of A/m
M has units of V/m
Then
(3-51)
(3-52)

## Slide 20
Line Distributed Current

## Slide 21
When J has units of Amps
M has units of Volts
Then
(3-53)
(3-54)

## Slide 22
Summary
Specify sources: electric current density J and magnetic current density M.
a. Find A (due to J) using
b. Find F (due to M) using

## Slide 23
The total electric and magnetic fields are then determined by
E=EA+EF
H=HA+HF

## Slide 24
Far-Field
D=Largest Dimension of the Antenna

## Slide 25
Far-Field

## Slide 26
In the far field region, only contributes the Er component (it contributes to the near field);
jωA contributes to all E components, including Er, E, and Eφ.
Since in far field region E and H are TEM wave, Er will be zero.- This requires that the Er contributions from and jωA must cancel each other in the far field region.
Conclusion: when calculating far E field, we only consider the contributions from jωA. – this shows the benefit of using auxiliary functions
*

## Slide 27
Same conclusion can be draw for the far H field due to magnetic current
when calculating far H field, we only consider the contributions from jωF
Above conclusion is widely used in the CEM software (such as those based on MoM), where the EM field is calculated in the far field region – this reduces the computing time.

## Slide 28
(for θ and φ components only)
(3-58a)
(for θ and φ components only)
(3-58b)
E and H fields due to J

## Slide 29
(for θ and φ components only)
(for θ and φ components only)
E and H fields due to M

## Slide 30
Uniqueness Theorem
Electromagnetics: Core Theorems
Duality
Principal
Equivalence
Theorem
Reciprocity
Theorem
Huygens’
Principal
Green’s Theorem

## Slide 31
Duality Theorem
When two equations that describe the behavior of two different variables are of the same mathematical form, their solutions will also be identical. The variables in the two equations that occupy identical positions are known as dual quantities and a solution of one can be formed by a systematic interchange of symbols to the other.
Electric current J and electric charge ρ
Magnetic current M and magnetic charge ρm
It must, however, be emphasized that this is purely mathematical, since it is known, as of today, that there are no magnetic charges or currents in nature

## Slide 32
Examples of Duality Theorem
Radiated E & H fields are known

## Slide 33
Reciprocity

## Slide 34
Reciprocity Theorems in Circuits
I2 V1= I1 V2
Reciprocity means
Z12= Z21
Port 1
Port 2
Port 1
Port 2

## Slide 35
Transmitting & receiving patterns are reciprocal provided the medium of wave propagation is linear.
A. We usually analyze patterns in the transmitting mode
B. We usually measure patterns in the receiving mode
Reciprocity Theorems for Antennas

## Slide 36
Reciprocity Theorems for EM Fields
In a linear and isotropic medium, there exist two sets of sources J1 and J2, which are allowed to radiate simultaneously or individually inside the same medium at the same frequency. J1 and J2 produces fields (E1, H1) and (E2, H2), respectively.
From Maxwell’s curl equations we can get
Lorentz Reciprocity Theorem in differential form
(3-60)
Taking a volume integral of both sides of (3-60) and apply divergence theorem
(3-61)
Lorentz Reciprocity Theorem in integral form
r

## Slide 37
Let S be a spherical surface and →∞ (S is in the far-field region of J1 & J2)
and
therefore
(3-61) is reduced to
TEM waves
r

## Slide 38
If both sources are constant line current I1 and I2
The unit of both sides is Watt, but they does not present the power, they are defined as Reaction

## Slide 39
Reciprocity of circuit
Z12= Z21
The equivalent circuit network of transmitting & receiving antennas system and its reciprocity
Beside the T & R antennas system, for any circuit system(including RLCG) with two ports, we can prove:
Maxwell’s curl equations->reciprocity of EM fields->reciprocity of circuit
Reciprocity of EM fields

## Slide 40
Antenna Arrangement for Pattern
Measurements & Reciprocity Theorem
V2oc = V1oc
The receiving mode of operation for the test antenna is most widely used to measure antenna patterns because the transmitting equipment is, in most cases, bulky and heavy while the receiver is small and lightweight

## Slide 41
Homework
Page 150